## Slide 1: ENGR 4220/5220: Control Systems
Rick Hill, PhD
Dept of Mechanical Engineering

## Slide 2: Lecture 1: Overview and Intro
Introduction to the control system design process
Control system example
  open loop vs. closed loop
Introduction to modeling
Solving differential equations
  Free response
  Forced response

## Slide 3: Control System Design Process
Translate
Plant
Design (and
Construction)
Model
Analyze
Controller Design
customer
input / gov’t
regulations
eng specs
physical
system
diagrams
math
behavior
control
system
purpose of models
analysis
design
verification
types of models
physical vs.
empirical
mathematical
graphical
types of analysis
time domain
frequency domain
simulation
hardware in the
loop (HIL)
types of control
supervisory
logic control
on/off control
P, PI, PD, PID
advanced
techniques

## Slide 4: Control System Example
Cruise Control Example
Control
Algorithm
Engine
Car
desired
speed
throttle
angle
(voltage)
force
actual
speed

## Slide 5: Open-loop Control [feedforward]
+
-
disadvantages
sensitive to errors
in model
sensitive to
disturbances
needs periodic
recalibration
advantages
simple to design
inexpensive
doesn’t affect
stability
fast response
wind force,
gravity force
Control
Algorithm
Engine
Car
throttle
angle
(voltage)
force
actual
speed
desired
speed

## Slide 6: Closed-loop Control [feedback]
disadvantages
extra complexity
extra cost
can affect stability
can be slow to
respond
advantages
robust to errors
in model
robust to
disturbances
+
-
wind force,
gravity force
Control
Algorithm
Engine
Car
throttle
angle
(voltage)
force
actual
speed
Speedometer
+
-
measured
speed
R
E
D
U
Y
CONTROLLER
ACTUATOR
PLANT
SENSOR
desired
speed

## Slide 7: Introduction to Modeling
A model is an abstraction of the physical world
Used for analysis and design, possibly before physical system exists
Can be obtained from first principles or experimentally
Purpose determines level of abstraction, form
Complex enough, but no more

## Slide 8: Model Derivation
From first principles
  Use physical laws to derive models
  Provides understanding
  Can use empirical data to determine parameters, validate model

## Slide 9: Model Derivation
From empirical data
  Feed a known input and observe output, fit model to data
  Good for complicated systems (IC engine, battery)
  Good for black-box systems (driver model)
  Does not provide intuition, can’t be widely applied
SYSTEM

## Slide 10: Complexity Depends on Purpose
Design/analysis model: simpler
  Simple enough to generate closed-form solution
  Less accurate, but provides intuition

## Slide 11: Complexity Depends on Purpose
Simulation model: more accurate

## Slide 12: Static vs. Dynamic Systems
Static Systems
Output is determined only by the current input, reacts instantaneously
Relationship does not change (it is static!)
Relationship is represented by an algebraic equation
Dynamic Systems
Output takes time to react
Relationship changes with time, depends on past inputs and initial conditions (it is dynamic!)
Relationship is represented by a differential equation
SYSTEM
input
output

## Slide 13: Static vs. Dynamic Systems
Motor from a Dynamic Viewpoint
Motor from a Static Viewpoint
speed
torque
T
Tstall
ea1
ea2
w
wno-load

## Slide 14: Solving Differential Equations
Homogenous differential equations
  Righthand side of equation equals 0
  Represents free response of system
  Solution consists of exponentials
  where exponents are roots of the characteristic eq.

## Slide 15: Solving Differential Equations
Homogenous differential equations
  For the above, the characteristic equation is
  Roots can be found from the quadratic formula

## Slide 16: Solving Differential Equations
Recalling that
If the roots are completely real, then the solution is exponential
  If all negative, stable
  If any positive, unstable
time
displacement, x

## Slide 17: Solving Differential Equations
If the roots are complex, then can rewrite in sines and cosines using Euler’s identity:
Therefore,

## Slide 18: Solving Differential Equations
Above follows when have complex roots of char. eq.
real part = rate of decay (growth)
imag part = freq of oscillation

## Slide 19: Solving Differential Equations
Forced differential equations
  Solution consists of two parts
  xh is the homogenous solution
  - same form as before, natural response of system
  xp is the particular solution
  - generally same form as F(t), due to the input

## Slide 20: Example
has a solution of the form
where
the homogenous portion dies out (transient)
the particular portion remains (steady state)
xh(t)
xp(t)

## Slide 21: Example
Consider other types of forcing functions:

## Slide 22: Example
Find the solution x(t) for

## Slide 23: Example
Find the solution x(t) for

## Slide 24: Example (continued)