## Slide 1: Lecture 5: Transfer Functions and Block Diagrams
Review differential equation solution process
Transfer function models
Intro to block diagrams
Intro to time response analysis (if time)

## Slide 2: Differential Equation Review
Recall, the Laplace transform converts LTI differential equations to algebraic equations
differential
equation
algebraic
equation
solve in time domain
solve in s-domain
X(s)
x(t)
L
L-1
1
2
3

## Slide 3: Differential Equation Review
Let’s determine the solution of the linear differential equation from last lecture
System has no damping, note that the roots of characteristic equation are purely imaginary
Can solve for θ(t) using the Laplace transform

## Slide 4: Example

## Slide 5: Example (continued)
The free response (f(t) = 0) is then
θ(t) is a shifted sinusoid of frequency ωn, called the (undamped) natural frequency
Now consider mass-spring-damper example from last time (which does have damping)

## Slide 6: Example

## Slide 7: Example (continued)
y(t) is a damped sinusoid with frequency 6 rad/sec … called the damped natural freq ωd
The (undamped) natural frequency ωn is frequency if the system has no damping

## Slide 8: Transfer Function Models
Often it is desired to remain in the Laplace domain for analysis and manipulation
The transfer function G(s) of a system is an alternative model to the differential equation and is defined as the ratio of the Laplace transform of the output Y(s) to the Laplace transform of the input U(s) assuming zero initial conditions

## Slide 9: Transfer Function Models
Characterize the input-output relationship of a dynamic system (ignores initial conditions)
Are a property of the system itself, not specific to the particular forcing input (represent natural response)
Have units, but do not provide information concerning the physical structure
Apply only to linear time-invariant (LTI) systems
Make combining systems much easier

## Slide 10: Finding a Transfer Function Model
Begin with
Choose what is the input and what is the output
Take Laplace transform assuming zero ICs
Rearrange

## Slide 11: Example
Find the equation of motion for the following system

## Slide 12: Example (continued)
Find the transfer function for the previous example where T(t) is the input and θ(t) is the output

## Slide 13: Block Diagrams
is often drawn as a block diagram
where U(s), Y(s) are signals and G(s) is a system
Mathematically, Y(s) = G(s)U(s)
In the time domain, need a convolution integral
U(s)
Y(s)
G(s)

## Slide 14: Block Diagrams
Useful for visualizing complex systems
+
-
wind force,
gravity force
Control
Algorithm
Engine
Car
throttle
angle
(voltage)
force
actual
speed
Speedometer
+
-
measured
speed
desired
speed

## Slide 15: Block Diagrams
Useful for visualizing complex systems
here each block is a transfer function and the arrows represent signal flow
+
-
C(s)
G(s)
P(s)
H(s)
+
-
R
Em
U
D
Y
Ym
Notes: Can get even more complicated than this … feedforward control … multiple feedback loops … other extraneous inputs like noise

## Slide 16: Time Response
Consider the TF from our earlier example
It is desired to find the time response θ(t) for different torque inputs
In general,

## Slide 17: Time Response
Impulse response –

## Slide 18: MATLAB Notes