## Slide 1: Lecture 23: Frequency Response for Design
Relationship between time response and frequency response
Bode plots for controller design
Robustness and optimality

## Slide 2: Relation Between Domains
Open-loop Frequency Response
Closed-loop Time Response

## Slide 3: Relation Between Domains
OL Bode indicates CL time response properties
  Steady-state performance:
    Larger gain at DC reduces steady state error
    DC gain of a type 0 system can be identified by the magnitude at small frequencies
    Slope of magnitude at small freq indicates system type
  Transient performance:
    Smaller resonant peak and larger phase margin indicate smaller overshoot
    Larger gain crossover frequency indicates faster response

## Slide 4: Example
Determine an additional gain K that will increase the given system’s phase margin to 45 degrees
What is the effect on the system’s response?

## Slide 5: Design with Frequency Response
Analyze time response behavior, determine deficiencies
Plot open-loop system’s frequency response
Add controller to change shape of frequency response plot
  For Bode plots, controller’s graph literally adds to the plant’s (reason to use the open-loop for design)
  Note: magnitude and phase plots are dependent
Iterate

## Slide 6: Design with Frequency Response
Step 2
Step 1

## Slide 7: Design with Frequency Response
Step 3

## Slide 8: Bandwidth
Most analysis and design in frequency domain is done using the open-loop
One exception is bandwidth, which is a measure of the system’s (closed-loop) speed of response (relates to gain crossover freq)
Definition:
Bandwidth is the frequency at which the closed-loop magnitude plot drops to -3dB below its DC magnitude

## Slide 9: Comparison
Advantages of Frequency Response
  Richer source of information
  Settles ambiguities from the root locus (higher-order dynamics, numerator dynamics)
  Good for experimental derivation
Advantages of Time Response
  Gives result directly in the time domain, ultimately what we want

## Slide 10: Other Considerations
So far, we have mostly been concerned with achieving the least amount of error
  Transient error
  Steady-state error
Other concerns
  Amount of control effort
  Robustness
Can define optimality in terms of a balance of these concerns

## Slide 11: Control Effort
Large control effort often means increased cost
  Means more power/fuel required
  Larger peak effort requires a larger actuator
In general, faster response requires more control effort

## Slide 12: Robustness
Robustness defines how well a system will perform in the presence of
  Measurement noise
  Disturbances
  Model uncertainty
  Time delays
In general, there is a tradeoff between robustness to various sources

## Slide 13: Robustness
Consider

## Slide 14: Robustness
Note, all three transfer functions have the same denominator
Also
Therefore, these transfer functions are not independent

## Slide 15: Robustness
For example,
Making C → ∞
  Gyd → 0
  Gyn → -1
Making C → 0
  Gyd → P
  Gyn → 0
Problem, can’t attenuate both noise
and disturbances at same time

## Slide 16: Robustness
One solution relies on the fact that our systems behave differently at different frequencies
Therefore, we will attenuate noise at high frequencies and disturbances at low frequencies
Desired open-loop magnitude plot is thus
ω(rad/sec)
M(dB)

## Slide 17: Robustness
This approach is also desirable because models tend to be most uncertain at high frequencies
ω(rad/sec)
M(dB)